## Slide 1
Integrated Solid Waste Management Kutaisi
– Accompanying Technical Training –
5th Training
“Municipal Waste Management Planning“
Collection logistics
Basics and planning advice
provided by Joerg Wagner, International Expert for Solid Waste Management

## Slide 2
1. Tasks of Waste Collection Planning
Unproblematic implementation of waste collection systems
Security of investment
Economic efficiency (optimizing the workload of vehicles and staff)
Balancing of operations

## Slide 3
Specifications set by municipalities
  collection system
  collection frequency
  waste amount generated, type of bins, number of emptying, filling degree inside the bins, bulk density of waste in the bin
Geographical characteristics
  structure of dwelling, population density
  road infrastructure
  average driving speed, obstacles on the collection route
Collection work
  vehicle technology
  staff
  working time scheme
  other logistical features
2. Influencing factors on collection logistics

## Slide 4
Specifications set by municipalities
  collection system
  collection frequency
  waste amount generated, type of bins, number of emptying, filling degree inside the bins, bulk density of waste in the bin
Geographical characteristics
  structure of dwelling, population density
  road infrastructure
  average driving speed, obstacles on the collection route
Collection work
  vehicle technology
  staff
  working time scheme
  other logistical features
2. Influencing factors on collection logistics

## Slide 5
Specifications set by municipalities
  collection system
  determination of collection frequency
2. Influencing factors on collection logistics
Collection system
Type of bin
Vehicle technology
Bring system
Depot container
1,5 -3,5 m³
Roll-off tipping vehicle with a crane
Front end loader,
Large refuse contai-
ners 60 - 240 l
Side loader
Pick-up systems
Collection of bundles
Rear end loader
with large feeding device
Rear end loader,
Large refuse contai-
ners 550 - 1.100 l

## Slide 6
Specifications set by municipalities
  collection system
  collection frequency
  waste amount generated, type of bins, number of emptying, filling degree inside the bins, bulk density of waste in the bin
Geographical characteristics
  structure of dwelling, population density
  road infrastructure
  average driving speed, obstacles on the collection route
Collection work
  vehicle technology
  staff
  working time scheme
  other logistical features
2. Influencing factors on collection logistics

## Slide 7
Geographical characteristics
  structure of dwelling, population density
2. Influencing factors on collection logistics
Opened apartment building structure DS 3
Large housing estates DS 1
Scattered rural dwelling DS 5
DS 2 Closed apartment building structure
DS 4 Single- or double-family housing area
Commercial and industrial areas

## Slide 8
Specifications set by municipalities
  collection system
  collection frequency
  waste amount generated, type of bins, number of emptying, filling degree inside the bins, bulk density of waste in the bin
Geographical characteristics
  structure of dwelling, population density
  road infrastructure
  average driving speed, obstacles on the collection route
Collection work
  vehicle technology
  staff
  working time scheme
  other logistical features
2. Influencing factors on collection logistics

## Slide 9
Collection work
  characteristic time steps
2. Influencing factors on collection logistics
Collection
Transportation
Set-up time, breaks
Emptying

## Slide 10
Collection work
  collection time
2. Influencing factors on collection logistics
Collection point 25 kg
25 sec.
Stretch of road:
length 100 m, through road, dwelling structure 4
No. 1
Collection point 25 kg
25 sec.
Collection point 50 kg
36 sec.
Emptied containers: Collection time: Waste amount collected:
5 187 sec. 125 kg
No. 2
No. 3
No. 4
No. 5
Interim Transport
16 sec.
Collection point 25 kg
25 sec.
Interim transport
16 sec.
Interim transport
28 sec.
Interim transport
16 sec.

## Slide 11
Collection work
  tipping time
2. Influencing factors on collection logistics
example: - residual waste - bin size 60-240 ltr. - dwelling structure 4
Rear-end loader 1+2
Rear-end loader 1+1
Side loader 1+0
Number of bins per collection point
Tipping time per bin [sec.]

## Slide 12
Collection work
  interim transport time
2. Influencing factors on collection logistics
Through road
Ring road
Dead end
one side collection
both side collection
1,5
1,0
2,0
2,0
2,6
2,0

## Slide 13
Collection work
  transport time to the landfill or transfer station
2. Influencing factors on collection logistics
Calculation of transport time by use of average speed
Type of road
Highway
National road
Rural road
Innercity main road
DS 4/5
DS 1/2/3
Average speed [km/h]

## Slide 14
Collection work
  further time requirements
2. Influencing factors on collection logistics
Emptying time at landfill/transfer station
optional: Time for exchange of swap containers
Set-up time (preparation of the truck, refueling), breaks

## Slide 15
Collection work
  Example of collection of large refuse containers vs. depot containers
2. Influencing factors on collection logistics
Rear-end loader 1+1 Side loader 1+0 Roll-off tipping vehicle
Collection time [h]
Interim transport
Transport to landfill
Collection time