## Slide 1
Integrated Solid Waste Management Kutaisi
– Accompanying Technical Training –
„waste generation and separate collection”
March 22 - 23, 2017
Presented by: The SWM training expert Mr. René Boesten, PEM

## Slide 2: Estimation of Generated Waste Amounts
1.a) Calculation on the basis of the number of inhabitants or commercial activities by the use of specific parameters
Creation of specific parameters for
inhabitants
public services (hospitals, schools, kindergartens)
commercial activities (offices, restaurants, cinemas, department stores, supermarkets, a.o.)
Calculation of the waste amounts according to the real figures of the inhabitants or specific activities in the municipality

## Slide 3: Estimation of Generated Waste Amounts
Creation of specific parameters for
Inhabitants
FS Kutaisi | Waste per day per person | Waste per year per person
Regional capital | 0.85 | 310
Urban > 10,000 | 0.70 | 256
Urban < 10,000 | 0.55 | 201
Rural | 0.40 | 146
Real data 2015 | Waste delivered at the landfill (ton) | Population 2015 | Collection efficiency | total waste | Waste per day per person | Waste per year per person
Kutaisi city | 54,000 | 147,635 | 90% | 48,600 | 0.90 | 330

## Slide 4: Estimation of Generated Waste Amounts
Long term forecast:
Inhabitants
Total population from Georgian statistics office
Population forecast:
Economic growth: 1% growth = 0.3% more waste
Tourism waste: 1 overnight stay = waste/day from resident
Pop growth rates | per year
Rural | -0.5%
Urban | 2.0%

## Slide 5
Estimation of Generated Waste Amounts
1.a) Calculation on the basis of the number of inhabitants or commercial activities by the use of specific parameters
Example from Bulgaria:
№ | Object | Accumulation norm |  |  |  | kg/m3
 |  | Yearly |  | Daily |  | 
 |  | kg | l | kg | l | 
1. | Hospital – 1 bed | 230 | 700 | 0,63 | 1,9 | 330
2. | Policlinics 1 person | - | - | 0,1 | 0,4 | 250
3. | Hotels - 1 person | 80 | 400 | 0,22 | 1,1 | 200
4. | Dormitory – 1 person | 100 | 330 | 0,28 | 0,93 | 300
5. | Kinder-garden – 1 bed | 70 | 235 | 0,19 | 0,78 | 300
6. | School – 1 pupil | 20 | 90 | 0,06 | 0,3 | 320
7. | Institute – 1 pupil | 26 | 120 | 0,09 | 0,4 | 220
8. | Cinemas – 1 seat | 20 | 90 | 0,06 | 0,3 | 220
9. | Offices – 1 person | 50 | 250 | 0,14 | 0,7 | 200
10. | Restaurant – 1 meal | - | - | 0,06 | 0,2 | 300
11. | Kitchenette – 1 meal | - | - | 0,03 | 0,1 | 300
12. | Department store for food – 1 m2 | 120 | 460 | 0,33 | 1,27 | 260
13. | Department store for industrial goods – 1 m2 | 30 | 150 | 0,08 | 0,4 | 200
14. | Tailor office – 1 person | 100 | 250 | 0,27 | 0,68 | 400
15. | Warehouses – 1 m2 | 35 | 70 | 0,09 | 0,19 | 500
16. | Markets – 1 m2 | 18 | 36 | 0,06 | 0,12 | 500

## Slide 6: Estimation of Generated Waste Amounts
Long term forecast:
  Waste from inhabitants
  Waste from tourists
  Waste from public services (hospitals, schools, kindergartens)
  Waste from streetcleaning and markets
  Waste from commercial activities (offices, restaurants, cinemas, department stores, supermarkets, etc.)

## Slide 7: Estimation of Generated Waste Amounts
Long term forecast and waste disposal costs:
Waste from:
  inhabitants => paid via waste service fee
  tourists => paid via contracts with hotels and service fee
  public services => paid via contracts or service fee
  streetcleaning and markets => paid via waste service fee
  commercial activities => paid via contracts or service fee

## Slide 8
Analysis of Waste Composition
How to get figures on Waste Composition?

## Slide 9
Analysis of Waste Composition
What it is good for?
to know material composition (recyclable components, harmful components)
to assess/be aware of treatment/safety needs
to understand where prevention should/can be exercised
to assess feasibility and efficient ways of separate collection
to determine other management measures and monitor effectiveness
to get note on changes/trends in the waste generation
to support waste estimations and/or verify available data
to educate people

## Slide 10
Waste prognosis – meaning and importance
What it is good for?
to know future waste amounts generated
to plan waste collection and waste treatment capacities
to understand the effects of waste management measures
to assess feasibility and efficient ways of separate collection
to get note on changes/trends in the waste generation
to educate people

## Slide 11: Waste calculation
Total waste =
Waste per capita * total population + non-household waste + tourism waste
Total waste =
Waste delivered at the landfill

## Slide 12
 | Waste delivered at the landfills (ton) | Waste calculated (tons) | 
Baghdati Municipality | 1,949 | 2,481 | 
Chiatura Municipality | 2,423 | 6,058 | 
Kharagauli Municipality | 845 | 2,239 | 
Kutaisi Municipality | 54,442 | 51,731 | More non-household waste?
Sachkhere Municipality | 6,664 | 7,514 | 
Samtredia Municipality | 8,396 | 11,326 | 
Terjola Municipality | 2,269 | 4,089 | 
Tkibuli Municipality | 2,227 | 3,519 | 
Tskaltubo Municipality | 4,836 | 9,639 | 
Zestaponi Municipality | 7,105 | 9,019 | 
Vani Municipality | 1,331 | 2,818 | 
Khoni Municipality | 2,716 | 3,743 | 

## Slide 13
 | Waste delivered at the landfills (ton) | Waste calculated (tons) | 
C. Ambrolauri | 1410.15 | 305 | 
Ambrolauri Municipality |  | 1,361 | 
Oni | 1185.1 | 652 | 
Tsageri | 1079.4 | 912 | 
Lentekhi | ?? | 1,194 | What happens with the waste?

## Slide 14
Approaching the subject of separate collection
must be addressed in quality and quantity in your WM plan (2019 deadline!)
due to 2019 deadline a matter of prognosis
Source: Boer et al. (2005): Waste Management Planning and Optimization
Waste prognosis – meaning and importance

## Slide 15: Impact of separate collection
Waste composition:
Waste categories | Minimum (%) | Maximum (%)
Paper and cardboard | 12.2 | 16.7
Glass bottles | 4.8 | 6.4
Scrap metal | 1.5 | 2.3
Polyethylene / Plastics | 13.6 | 17.5
Sanitary paper/diapers | 4.8 | 8.3
Textiles | 5.4 | 5.9
Organic | 38.6 | 42.7
Construction waste | 4.0 | 4.1
Hazardous household waste | 1.4 | 1.7
Leather/rubber | 1.7 | 2.7
Other | 1.4 | 2.1
Loss (humidity) | 0.3 | 1.5

## Slide 16: Impact of separate collection
Estimated amounts of recyclables in municipal waste | Paper (t/a) |  | Glass (t/a) |  | Plastics (t/a) | 
 | lower limit | upper limit | lower limit | upper limit | lower limit | upper limit
Imereti | 12,447 | 20,596 | 4,852 | 7,837 | 13,885 | 21,603
Racha-Lechkhumi | 569 | 1,073 | 222 | 408 | 635 | 1,126
Estimated amounts of recyclables in municipal waste

## Slide 17: Impact of separate collection
Targets for collection |  |  | 
 | 2020 | 2025 | 2030
Paper | 30% | 50% | 80%
Glass | 20% | 50% | 80%
Plastic | 30% | 50% | 80%
waste composition |  | 
paper | 12.2% | 16.7%
glass | 4.8% | 6.4%
plastics | 13.6% | 17.5%
bio | 38.6% | 42.7%

## Slide 18: Impact of separate collection
 |  | Waste calculated (tons) | 2020 | 2025 | 2030 | difference
Baghdati Municipality |  | 2,481 | 2,266 | 2,102 | 1,874 | 
Chiatura Municipality |  | 6,058 | 5,662 | 5,131 | 4,575 | 
Kharagauli Municipality |  | 2,239 | 2,035 | 1,896 | 1,691 | 
Kutaisi Municipality |  | 51,731 | 49,033 | 43,816 | 39,067 | 
Sachkhere Municipality |  | 7,514 | 7,044 | 6,364 | 5,674 | 
Samtredia Municipality |  | 11,326 | 10,664 | 9,593 | 8,553 | -25%
Terjola Municipality |  | 4,089 | 3,792 | 3,463 | 3,088 | 
Tkibuli Municipality |  | 3,519 | 3,251 | 2,981 | 2,658 | 
Tskaltubo Municipality |  | 9,639 | 9,062 | 8,164 | 7,279 | 
Zestaponi Municipality |  | 9,019 | 8,473 | 7,639 | 6,811 | 
Vani Municipality |  | 2,818 | 2,585 | 2,387 | 2,128 | 
Khoni Municipality |  | 3,743 | 3,464 | 3,171 | 2,827 | 

## Slide 19: Impact of separate collection
 |  | Waste calculated (tons) | 2020 | 2025 | 2030 | difference
C. Ambrolauri |  | 305 | 199 | 258 | 230 | 
Ambrolauri Municipality |  | 1,361 | 1,202 | 1,153 | 1,028 | 
Oni |  | 652 | 529 | 553 | 493 | -25%
Tsageri |  | 912 | 775 | 772 | 689 | 
Lentekhi |  | 1,194 | 1,043 | 1,012 | 902 | 

## Slide 20: Impact of separate collection
Biowaste
  Kitchen, gardens, parks
  Composition: urban: 35 - 40%
            Rural: 45 – 60%
Collection / prevention
    Urban: 30 - 40% (mainly collection)
    Rural: 50 – 60% (mainly prevention)