## Slide 1
Integrated Solid Waste Management Kutaisi
– Accompanying Technical Training –
Sustainability in composting projects Compost quality and other issues
Training seminar for Municipalities & Services responsible for managing municipal waste (MSW) in the Imereti and Racha-Lechkhumi-Kmevo Svaneti region of Georgia with a particular focus on the mountainous municipalities
Jan Reichenbach
INTECUS GmbH, AMC Expert team Solid Waste Management

## Slide 2
Public acceptance
Proper siting approach
Well-organized collection ( input quality and quantities)
High operational standards and safety
Public benefits ( supplies of compost, transparent transfer of savings)
Market acceptance
Existence of offtakers
Product quality/safety
Preparedness to learn and adjust
Ensuring sustainability
Key sustainability aspects in composting projects
Compost quality is decisive for the success of a composting initiative! It requires utmost attention from its very beginning.

## Slide 3
has to include:
land and infrastructural suitability
distance to neighborhood
transportation routes
public engagement process
Public acceptance
Proper siting
Well-organized collection
has to take account of:
convenience issues
minimum nuisance
proper information
certain regularity (service and supply)
High operational standards and safety
see corresponding information provided on composting practice & quality issues
Public participation
must involve:
a sharing mechanism (information, product, financial)

## Slide 4
Safe compost can be produced from source separated biodegradable material only!
Unprocessed mixed household waste (MHW)
Samples from composting
Processed MHW
Biodegradable part separated from mixed household waste
Source-separated biodeg. w
German quality assurance BGK
Quality 1
Quality 2
Proposed Syrian standard
Lead
Cadmium
Chromium
Copper
Nickel
Mercury
Zinc
Market acceptance
Input determines output

## Slide 5
Value indicators
Rotting degree (state of material decomposition)
Bulk density
Salt content/ pH-value
Concentration in plant nutrients
Carbonats
Organic matter content
Quality features
Product quality = value of compost + adherence to precautionary criteria
Environmental safety/acceptance
Material hygiene (presence of salmonellae)
Viable weeds/seeds
Potential toxic substances (heavy metals)
Other undesired matter
Degree of visible pollution

## Slide 6
Quality standards
Environmental safety
Parameter | Class 1 | Class 2
Impurities (glass, metals, plastics (%) | <0.5 | 0.5
Lead mg/kg dm | 100 | 150
Cadmium mg/kg dm | 1.0 | 1.5
Chromium mg/kg dm | 70 | 100
Copper mg/kg dm | 70 | 100
Nickel mg/kg dm | 35 | 50
Mercury (mg/kg dm | 0.7 | 1.0
Zinc mg/kg dm | 300 | 400
Viable seeds and sprouting plant parts | 2 seeds/l | 
Parameter | EC comm. 834/2007 | EU eco-label
Impurities (glass, metals, plastics (%) | - | <0.5
Lead mg/kg dm | 45 | 100
Cadmium mg/kg dm | 0.7 | 1.0
Chromium mg/kg dm | 70 | 100
Copper mg/kg dm | 70 | 100
Nickel mg/kg dm | 25 | 50
Mercury (mg/kg dm | 0.4 | 1.0
Zinc mg/kg dm | 200 | 300
German RAL-standard (limiting values)
EU-level recommendation

## Slide 7
Quality standards
Compost value
Quality criteria | Parameter | Applicable requirements
Organic matter | Loss of ignition (mass-%) | >15 fresh c. / >30 mature c.
Dry matter | Dry matter (mass-%) | >55
Nutrients | N, P2O5, K2O, MgO, S (%) | to be declared
Alkaline effective matter | CaO (%) | to be declared
Nitrogen soluble | NH4-, NO3- (mg/l dm) | to be declared
Salt content | (g/l dm) | to be declared
pH-value |  | to be declared
Rotting degree | Degree centigrade | 60-40 fresh c. / <40 mature c.
Example: Provisions as per German quality assurance

## Slide 8
Quality standards
Limiting values and reality
Example: Results of German quality assurance monitoring

## Slide 9
1. Stipulations on operating conditions
Requirements to make sure sanitization/product hygiene
Composting facilities ensure material is exposed to 55 °C for two weeks or 65°C for one week (60°C in closed plants) [e.g. via legislation, German BioAbfV]
Securing safety of compost/compost use @ Process stage
- Human and veterinary hygienic aspects (salmonellae) - Phyto hygienic aspects (tobacco mosaic virus, clubroot (plasmodiophora brassicae), tomato seed
3. Direct Process Validation
Dumping and retrieval of test and indicator organisms
Continuous temperature management; every working day or automatically in three representatives zones
2. Process Supervision
- Salmonellae - Germinative seeds and reproducible plant parts
4. Final Product Analysis
Continous examinations of the final product

## Slide 10
Securing safety of compost/compost use @ application
Stipulations on application requirements
Example: German practice
Total (dry matter) amount applied per hectare within a period of three years shall not exceed:
Class 1 compost: 30 tons
Class 2 compost: 20 tons
Further restrictions: Treated separately collected biowaste from households is not allowed for application on permanent grassland.
Further ways to get precautionary regulations for compost use covered:
Fertilizer regulation -relevant for agriculture and gardening
Soil protection regulations
Regulation on Organic Farming

## Slide 11
For example by installation of a self-obligatory measure of the industry which legal authorities formally recognize
70 % of the compost produced in Germany gets the quality label RAL-GZ 251
Institutionalisation of quality assurance
In Germany since 1989: Quality Assurance Organisation for Compost Bundesgütegemeinschaft Kompost e.V. (BGK), established RAL quality assurance for compost (1991); RAL-quality labels identify a standardised and regularly checked product
Source: BGK, 2009

## Slide 12
Source: BGK, 2009
Objectives of the institutionalisation
Market acceptance / User safety
Specification of products with a guaranteed homogenous quality
Guarantee for a successful use of the products
Promotion
Enhancement of product quality and operation quality (increased reputation)
Promotion of the re-use of waste "from waste to product“ (SWM support)
Safety and Ease for Operators
Deregulation
Recognition of certified products by legal authorities, in agricultural systems and by food processing industry

## Slide 13
Compost market
Example: RAL-labelled compost products in Germany
Offtakers structure for facility produced compost
Source: BGK, 2009

## Slide 14
Preparedness to learn and adjust
The importance of piloting!
Decentralized aerobic composting of urban solid waste: Some lessons learned from Asian-EU Co-operative Research. Global NEST Journal, Vol 12, No 4, pp 343-351, 2010
Waste Composting in Kutaisi
funded by Royal Netherlands Embassy in Georgia, 1.09.2006-1.09.2007, GEL 16,890

## Slide 15
Preparedness to learn and adjust
Lessons learned ?
Sustainable use of biogenous household waste through aerobic treatment of separately collected organic waste and the application of compost in South Caucasian agriculture. Nikolas Zöller, Faculty of Organic Agricultural Sciences, University of Kassel, Witzenhausen, 2017

## Slide 16
Preparedness to learn and adjust
Lessons learned ?
10 ნოემ 2016 http://www.marneuli.gov.ge/marneulis-shesaxeb/siaxleebi1/1331-chexi-eqspertis-morigi-viziti-marneulshi.html

## Slide 17
Preparedness to learn and adjust
Its worth figuring out
EU and Government launch pilot green waste separation, collection and recycling project in Marneuli. Pilot will demonstrate how to utilise the green waste that fills 50% of regional landfills and help diminish production of Green House Gases https://eeas.europa.eu/delegations/georgia/59702/node/59702_lv
https://www.facebook.com/europeanunioningeorgia/videos/marneuli-waste-project/2067451053551138/